SECTION 32 14 13.19

CONCRETE GRID PAVEMENTS

(Section 02795)

Note: This guide specification for U.S. applications is for concrete grid units placed on a sand bedding course over a compacted dense-graded aggregate base. The text allows an option of topsoil and grass in the grid openings over bedding sand or No. 8 open-graded aggregate in the grid openings and for the bedding course. This specification is for limited vehicular applications such as access roads and emergency fire lanes, as well as intermittently used overflow parking areas. This text must be edited to suit specific project requirements for projects. This Section includes the term “Architect.” Edit this term as necessary to identify the design professional in the General Conditions of the Contract.

If the area is exposed to recurring vehicular traffic and additional stormwater storage in the base is desired, the specifier should consider using permeable interlocking concrete pavements, as they provide additional structural support to vehicles while providing runoff storage in an open-graded, crushed stone base. In such cases, the specifier should refer to the ICPI manual, Permeable Interlocking Concrete Pavements.

This product guide specification is provided by the Interlocking Concrete Pavement Institute.  Revisions made to the original guide specification were made solely by Genest Concrete Works, Inc., and are not endorsed by the ICPI.  This product guide specification is distributed by Genest Concrete Works, Inc. to assist in specifying the manufacturer’s products.

PART 1    GENERAL

1.01		SUMMARY

A.		Section includes:

1.  Concrete grid units.

2.  Bedding sand.

3.  Edge restraints.

4.  Geotextiles.

5.  [Topsoil and grass for the grid openings.]

6.  [Open-graded aggregate for the grid openings.]

7.  [Open-graded aggregate bedding course].

B.	 	Related Sections:

1.  Section [______]: Curbs and drains.

2.  Section [______]: Dense-graded aggregate base.

3.  Section [______]: Open-graded aggregate base.

1.02		REFERENCES

A.		American Society of Testing Materials (ASTM)

1.  C 33, Specification for Concrete Aggregates.

2.  C 136, Method for Sieve Analysis for Fine and Coarse Aggregate.

3.  C 140, Standard Test Methods of Sampling and Testing Concrete Masonry Units.

4.  C 979, Standard Specification for Pigments for Integrally Colored Concrete.

5.  C 1319, Standard Specification for Concrete Grid Paving Units.

6.  ASTM D 698, Standard Test Method for Laboratory Compaction Characteristics of Soil

Using Standard Effort (12,000 ft-lbf/ft3 (600 kN-m/m3)).

7.  D 2940, Standard Specification for Graded Aggregate Material for Bases or Subbases for Highways or Airports.

8.  D 5268, Specification for Topsoil Used for Landscaping Purposes.

B.		Interlocking Concrete Pavement Institute (ICPI)

1. Tech Spec technical bulletins.

1.03		SUBMITTALS

A.		In accordance with Conditions of the Contract and Division 1 Submittal Procedures Section.

B.		Manufacturer’s drawings and details: Indicate perimeter conditions, relationship to adjoining materials and assemblies, expansion and control joints, paving slab [layout,] [patterns,] [color arrangement,] installation [and setting] details.

C.		Sieve analysis per ASTM C 136 for grading of bedding and base materials.

Note: Include D below if the grid openings will be filled with topsoil and grass seed, or sod plugs.

D.		Source and content of topsoil and grass seed [sod].

E.		Concrete grid units:

1.  Color selected by Architect.

2.  [Four] representative full-size samples of each grid type, thickness, color, finish that indicate

the extremes of color variation and texture expected in the finished installation.

3.  Accepted samples become the standard of acceptance for the work.

4.  Test results from an independent testing laboratory for compliance of grid paving unit

requirements to ASTM C 1319.

5.  Manufacturer’s certification of concrete grid units by ICPI as having met applicable ASTM s				     standards.

6.  Manufacturer’s catalog literature, installation instructions, and material safety data sheets for

the safe handling of the specified materials and products.

F.     	LEED Submittals:

1.  Manufacturer shall provide product certificate for credit MR 4.1 materials and resources recycled content 5%.  Use concrete pavers with supplementary cementing materials such as fly ash or slag.

2.  Manufacturer shall provide product certificate for credit MR 4.2 materials and resources recycled content 10%.  Use concrete pavers with supplementary cementing materials such as fly ash or slag.

3.  Manufacturer shall provide certificates for credit MR 5.1 materials and resources regional materials.  Use locally manufactured concrete pavers and aggregate materials.

4.  Manufacturer shall provide product certificates for credit MR 5.2 materials and resources regional materials.  Use locally extracted materials for pavers and base.

5.  Manufacturer shall provide product certificates for credit SS 7.1 sustainable sites heat island effect.  Use concrete grid pavement or less than 29 SRI concrete paving units.

1.04		QUALITY ASSURANCE

A.		Manufacturer Qualifications:

1.  Paver manufacturer shall be an Interlocking Concrete Pavement Institute Certified Producer.

2.  Paver manufacturer shall be a member in good standing with the National Concrete Masonry Association.

3.  Paver manufacturer shall provide systematic testing of concrete pavers during production by a National Concrete Masonry Association Certified Masonry Testing Technician.

4.  Paver manufacturer shall provide independent quality assurance test results for concrete pavers manufactured and tested within a calendar year.

B.		Paving Subcontractor Qualifications:

1.  Engage an experienced installer who has successfully completed grid pavement installations

similar in design, material, and extent indicated for this Project.

2.  Hold a current certificate from the Interlocking Concrete Pavement Institute Concrete Paver

Installer Certification program.

C.		Single-source Responsibility: Obtain each color, type, and variety of grids, joint materials and

setting materials from single sources with resources to provide products and materials of

consistent quality, appearance and physical properties without delaying progress of the Work.

D.		Regulatory requirements and approvals: [Specify applicable licensing, bonding or other

requirements of regulatory agencies.]

E.		Mock-up

1.  Locate where directed by the Architect.

2.  Notify Architect in advance of dates when mock-ups will be erected.

3.  Install minimum [100] sf ([10] m2) of concrete grid units.

4.  Use this area to determine the quality of workmanship in to be produced in the final unit of

Work including surcharge of the bedding sand layer, joint sizes, lines, pavement laying

pattern(s), color(s), and texture.

5.  This area shall be used as the standard by which the work is judged.

6.  Subject to acceptance by the owner, mock up may be retained as part of the finished work.

7.  If mock up is not retained, remove and properly dispose of.

1.05		DELIVERY, STORAGE, AND HANDLING

A.		General: Comply with Division 1 Product Requirement Section

B.		Deliver concrete grid units to the site in steel banded, plastic banded, or plastic wrapped  packaging capable of transfer by forklift or clamp lift. Unload grids at job site in such a manner that no damage occurs to the product or existing construction.

C.		Cover sand with waterproof covering to prevent exposure to rainfall or removal by wind. Secure the covering in place.

D.		Coordinate delivery and paving schedule to minimize interference with normal use of buildings adjacent to paving.

1.06  		ENVIRONMENTAL CONDITIONS

A.		Do not install bedding materials or grid units during heavy rain or snowfall.

B.		Do not install bedding materials and grid units over frozen base materials.

C.		Do not install frozen bedding materials.

1.07      GRID MAINTENANCE MATERIALS

A.		Supply [     ] sf  [(   m2)] of [each type and color of grid unit] in unopened pallets with contents labeled. Store where directed.

B. 		From the same production run as installed materials.

PART 2    PRODUCTS

2.01   	CONCRETE GRID UNITS

A.		Manufacturer: Genest Concrete Works, Inc.

1.  Contact: Genest Concrete Works, Inc. 36 Wilson Street, Sanford, Maine 04073, phone: 1-800-332-4773, fax: 1-207-490-5076, www.GenestConcrete.com. Email: jlenzen@genest-concrete.com

B.		Concrete grid units, including the following:

1.  Grid unit type: Duragreen.

a.  Material standard: Comply with material standards set forth in ASTM C 1314.

b.  Color: [Natural], [Custom]

c.  Color Pigment Material Standard: Comply with ASTM C 979.

d.  Size: 23-3/4” x 15-3/4” x 3-5/8” thick.

C.		Manufactured in a plant where paving products are certified by ICPI as having passed ASTM

requirements in this specification.

2.02		PRODUCT SUBSTITUTIONS

A. 		Substitutions: No substitutions permitted.

2.03 		BEDDING MATERIALS

Note: If openings are filled with topsoil, use sand bedding. If the openings are filled with open-graded aggregate for additional runoff storage, the same aggregate should be used for the bedding. Edit 2.03 and 2.04 accordingly.

A.		General – Sieved per ASTM C 136.

B.		Bedding Sand

Note: The type of sand used for bedding is often called concrete sand. Sands vary regionally. Contact

contractors local to the project and confirm sand(s) successfully used in previous similar applications

Bedding sand is not used in ditch liner applications, slope protection, riparian stabilization or with boat ramps

constructed with concrete grid units.

1.  Washed, clean, hard, durable crushed gravel or stone, free from shale, clay, friable

materials, organic matter, frozen lumps, and other deleterious substances.

2.  Conforming to the grading requirements in Table 1 below.

3.  Do not use limestone screenings.

Table 1

ASTM C 33 Gradation for Bedding Sand

Sieve Size  		Percent Passing

3/8 in. (9.5 mm)		100

No. 4 (4.75 mm)	95 to 100

No. 8 (2.36 mm	)	85 to 100

No. 16 (1.18 mm)	50 to 85

No. 30 (0.600 mm)	25 to 60

No. 50 (0.300 mm)	10 to 30

No. 100 (0.150 mm)	2 to 10

No. 200 (0.075 mm)	0 to 1

-OR-

B.		Washed, open-graded stone.

Note: Finer gradations such as ASTM No. 89 stone may be used.

1. Conforming to the grading requirements in Table 2 below.

Table 2

ASTM No. 8 Gradation for Bedding and Joint/Opening Filler

Sieve Size		Percent Passing

12.5 mm (1/2 in.)	100

9.5 mm (3/8 in.)		85 to 100

4.75 mm (No. 4)	10 to 30

2.36 mm (No. 8)	0 to 10

1.18 mm (No. 16)	0 to 5

2.04		FILL MATERIALS FOR GRID OPENINGS

A.		Topsoil: Conform to ASTM D 5268.

Note: Consult with local turf grass specialists for recommendations on grass seed mixture or sod materials.

B.		Grass seed [Sod]: [mixture and source].

-OR-

A.		Open-graded aggregate.

B.		Conforming the gradation requirements in Table 2. Do not use gravel.

2.05		EDGE RESTRAINTS

A.		Provide edge restraints installed around the perimeter of all concrete grid paving unit areas as follows:

1.  Manufacturer: Gator Edge, manufactured by Alliance Designer Products Inc., Laval, Quebec 866-212-1611, Supplied by Genest Concrete Works, Inc.

2.  Manufacturer:  Structure Edge, Brick Block, manufactured by Permaloc Corporation, Holland, MI 800-356-9660.  Supplied by Genest Concrete Works, Inc.

3.  Material: [Plastic] [Concrete] [Aluminum] [Steel] [Precast concrete] [Cut stone].

4.  Material standard: [Specify material standard].

5.  Or approved equal.

2.06		ACCESSORIES

A.		Provide accessory materials as follows:

1.  Geotextile fabric:  Manufactured by: Synteen Technical Fabrics, Lancaster, SC 800-796-8336  Supplied by Genest Concrete Works, Inc.

2. Geotextile fabric: Manufactured by: SRW Products, Princeton, MN 800-752-9326.  Supplied by Genest Concrete Works, Inc.

a.  Material Type and Description: [Specify material type and description].

b.  Material Standard: [Specify material standard.].

3.  Or approved equal.

PART 3     EXECUTION

3.01		ACCEPTABLE INSTALLERS

A.		Engage an experienced installer who has successfully completed paver installations similar in design, material, and extent indicated for this project.

B.		Hold a current certificate from the Interlocking Concrete Pavement Institute, concrete paver installer certification program.

C.		[Specify acceptable paving subcontractors.].

3.02	EXAMINATION

Note: Compaction of the soil subgrade is recommended to a minimum of 95% standard Proctor density per ASTM D 698 for pedestrian and lightly trafficked vehicular areas. Stabilization of the subgrade and/or base material may be necessary with weak or saturated subgrade soils.

Note: Local aggregate base materials typical to those used for highway flexible pavements are recommended, or those conforming to ASTM D 2940. Compaction of aggregate is recommended to not less than 95% Proctor density in accordance with ASTM D 698 is recommended for pedestrian and vehicular areas. Mechanical tampers are recommended for compaction of soil subgrade and aggregate base in areas not accessible to large compaction equipment. Such areas can include that around lamp standards, utility structures, building edges, curbs, tree wells and other protrusions. The recommended base surface tolerance should be ±3/8 in. (±10 mm) over a 10 ft. (3 m) straight edge.

Note: The elevations and surface tolerance of the aggregate base determine the final surface elevations of concrete grids. The installation contractor cannot correct deficiencies in the base surface with additional bedding materials. Therefore, the surface elevations of the base should be checked and accepted by the General Contractor or designated party, with written certification to the paving subcontractor prior to placing bedding materials and concrete grids.

A.		Acceptance of site verification conditions:

1.  Contractor shall inspect, accept and verify in writing to the grid installation subcontractor that

site conditions meet specifications for the following items prior to installation of bedding

materials and concrete grid units:

a.  Verify that drainage and subgrade preparation, compacted density and elevations conform to specified requirements.

b.  Verify that geotextiles, if applicable, have been placed according to drawing and specifications.

c.  Verify that base materials, thickness, [compacted density,] surface tolerances and elevations conform to specified requirements.

d.  Provide written density test results for the soil subgrade, base materials to the Owner, Contractor, and grid installation subcontractor.

2.  Do not proceed with installation of bedding materials and concrete grids until [subgrade soil

and] base conditions are corrected by the Contractor or designated subcontractor.

3.03		PREPARATION

A.		Verify that base is dry, certified by Contractor as meeting material, installation and grade

specifications [and geotextile] are ready to support sand, [edge restraints,] grids and imposed

loads.

B.		Edge Restraint Preparation:

1.  Install edge restraints per the drawings [and manufacturer’s recommendations] [at the

indicated elevations.].

2.  Mount directly to finished base. Do not install on bedding sand.

3.  The minimum distance from the outside edge of the base to the spikes shall be equal to the

thickness of the base.

3.04  		INSTALLATION

A.		Spread the sand [No. 8 stone] evenly over the compacted, dense-graded base layer and

screed uniformly to 1/2 to 1 in. (13 to 25 mm). Place sufficient sand [stone] to stay ahead of

the laid grids.

B.	 	Ensure the grid units are free from foreign materials before installation.

C.	 	Lay the grid units on the bedding sand in the pattern(s) shown on the drawings. Maintain

straight joint lines.

D.	 	Joints between the grids shall not exceed [3/16 in. (5 mm)].

E.		Fill gaps at the edges of the paved area with cut grids or edge units.

F.  		Cut grids to be placed along the edge with a double-bladed splitter or masonry saw.

G.		Sweep [top soil][No. 8 aggregate] into the joints and openings until full.

H.		Sweep the grid surface clear prior to compacting.

I.		Compact and seat the grids into the screeded [bedding sand] [No. 8 aggregate] using a low-amplitude, 75-90 Hz plate compactor capable of at least 4,000 lbs. (18 kN) centrifugal compaction force. Use rollers or a rubber or neoprene pad between the compactor and grids to prevent cracking or chipping. Do not compact within 6 ft (2 m) of the unrestrained edges of the grid units.

J.		All work to within 6 ft (2 m) of the laying face must be left fully compacted at the completion of each day.

K.		[Broadcast grass seed at the rate recommended by seed source.][Place sod plugs into openings.] [Add topsoil to the surface to cover the seeds.]

L.		Remove excess [topsoil][No. 8 aggregate] on surface when the job is complete.

M.		[Distribute straw covering to protect germinating grass seed [sod]. Water entire area. Do not 			traffic pavement for [30] days.] if seeded.

3.05   	FIELD QUALITY CONTROL

A.		After removal of excess top soil/aggregate, check final elevations for conformance to the drawings. Allow 1/8 to 1/4 in. (3 to 6 mm) above specified surface elevations to compensate for minor settlement.

B.		The final surface tolerance from grade elevations shall not deviate more than ±3/8 in. (10 mm) over a 10 ft (3 m) straightedge.

C.		The surface elevation of grid units shall be 1/8 to 1/4 in. (3 to 6 mm) above adjacent drainage inlets, concrete collars or channels.

D.		Lippage: No greater than 1/8 in. (3 mm) difference in height between adjacent grid units.

3.06		PROTECTION

A.		After work in the section is complete, the Contractor shall be responsible for protecting work from damage due to subsequent construction activity on the site.

END OF SECTION